The Town of Mount. Pleasant is seeking bids for (1) latest model 2021 F-350 SRW Manufacture Code (F3B) 4X4 Pickup Truck Regular Cab, 8’ Box, including all standard equipment. All vehicles, components, and accessories are to be new, unused. All specifications are to be considered minimum.

2021 F-350, SD Regular Cab Painted White

4x4 SD Regular Cab 8' box 142" WB SRW XL (F3B)

Major Equipment

6.2L V-8 SOHC w/SMPI 385hp v8 Flex Fuel

TorqShift 6 speed automatic w/OD (6R140)

* 4-wheel ABS							* Brake assistance

* Traction control 						* LT 245/75R17 E BSW AS S-rated tires

* Battery with run down protection				* Firm suspension

* Advance Trac w/Roll Stability Control 				* Air conditioning

* Tinted glass							* AM/FM stereo with seek-scan

* Daytime running 						* Dual manual mirrors

* Variable intermittent wipers				 	* 17 x 7.5 steel wheels

* SecuriLock immobilizer 	* Tachometer

* Message Center 						* Reclining front split-bench seats

* Steering-wheel mounted audio controls 			* Class V hitch

* Front axle capacity: 6000 lbs. 					* Rear axle capacity: 7280 lbs.

* Front spring rating: 4400 lbs. 					* Rear spring rating: 6340 lbs.

* Frame section modulus: 10.7 cu.in. 				* Frame Yield Strength 50000 psi

* Cab to axle: 56.1"

* Dual front airbags w/passenger cancel

* Driver and front passenger seat mounted side airbags

With Standard truck options:

* GVWR: 10,300 lb. Payload Package 				* Spare Tire, Wheel, Carrier & Jack

* Tires: LT275/70RX18E BSW A/T (4) 				* Power Equipment Group

* Wheels: 18" Argent Painted Steel 				* Snow Plow Prep Package

* HD Vinyl 40/20/40 Split Bench Seat 				* Platform Running Boards

* Green	 Standard paint 						* Tough Bed Spray-In Bedliner

*913 Radio with Sync						*110V400W Outlet

* 50-State Emissions System 					* Upfitter Switches (6)

* Front Splash Guards/Mud Flaps 				* Rear Splash Guards/Mud Flaps

*Upfitter Interface Module					* 3.73 Axle Ratio

* Bed Step	* Tailgate Step & Handle

Aftermarket Options:

(1) One 8’ Western pro plus plow Installed with Nighthawk LED lamps, and Snow Deflector

(1) Aluminum deep Crossed toolbox (Defender Series by Weather Guard)

All Components to be new and vehicle is to be delivered to the Town of Mount Pleasant 596 Columbus Ave Thornwood NY 10594